## Slide 1: 3-IBFE 3D Flow Past Objects

## Slide 2: Goal
Create a plate in a 3D flow tank.
Let the plate be tethered along its centerline.
Let the plate have 2 stiffnesses (middle half is different than ends).
Move the flow from left to right along x-axis.
Download here: https://drive.google.com/open?id=0B4mLG2SPb-tbQkVXRkVxV05vZ00

## Slide 3: Strategy for domain and plate dimensions
In this example, the domain is 32x16x16 units.
The domain goes from -16<x<16, -8<y<8, -8<z<8.
dx = 16/256 = 0.0625.
Make a plate that is 0.125 x 2 x 2 units.
Position the plate with center at origin, and then translate 7 units in the negative x-direction.

## Slide 4: Step 1: Make the mesh in gmsh
The resulting file should be similar to plate2.msh in the Example folder.
Remember that we want the element size to be about dx=0.0625.
We can make this by making a square and then extruding it into the third dimension.

## Slide 5: Open gmsh, then File-> new
Go to Geometry-> Elementary entities -> Add -> Point
Make points at (0,1,1), (0,-1,1), (0,-1,-1) and (0,1,-1) with Prescribed mesh element size set to 0.0625.
Click Add for each point.

## Slide 6: Connect the points with lines
Go to Geometry-> Elementary entities-> Add-> Straight Line
Left click one point and then the next to make a line.
Repeat for all 4 sides.
Left click and drag to rotate the image in 3D.

## Slide 7: Make a surface from the square
Geometry-> Elementary entities -> Add->Plane Surface
Left click a line to illuminate the hole square.
Press e to end selection.
A grid should appear over the plane.

## Slide 8: Extrude to 3D plate
Geometry-> Elementary entities -> Add -> Translate -> Extrude surface
Extrude 0.125 in x-direction.
Left click grid so it’s red.
Press e to end.
This will make plate 2 elements thick.

## Slide 9: Make a volume in the frame
Geometry-> Add -> Elementary entities -> Add -> Volume
Select dashed grid lines so the glow red, click e to end.

## Slide 10: Add a physical group that is the volume
Geometry->Physical Groups -> Add -> Volume
In the popup box, name your mesh and use automatic numbering.
Left click the yellow dot in the middle of box.
Press ‘e’ to end.

## Slide 11: Make the mesh
Mesh -> 3D
File -> save mesh
The above will save the mesh of the physical group as group_name.msh. This leaves only the 3D mesh and no 1D or 2D meshes that libmesh will reject.

## Slide 12: input3d
In this example, the mesh name is given in the input3d file. [LM: the mesh name also appears in the main.C file, but I think those lines are obsolete, will check].
Re is modified by updating the viscosity accordingly.
Flow ramps up from 0 m/s at t = 0 and moves in the x-direction.

## Slide 13: main.C - Translate FE boundary
We made our FE mesh at the origin. We want to shove the plate left so it’s at the beginning of the flow tank.The coordinate_mapping_function does this.
void coordinate_mapping_function(libMesh::Point& X, const libMesh::Point& s, void* /*ctx*/)
{
X(0) = s(0) - 7; // translated 7 units left along x-axis
return;
}

## Slide 14: main.C- Target forces
void target_force_function(VectorValue<double>& F, const TensorValue<double>& /*FF*/,
const libMesh::Point& X, const libMesh::Point& s, Elem* const /*elem*/,
const vector<NumericVector<double>*>& /*system_data*/, double time, void* /*ctx*/)
{
libMesh::Point s_dump;
double kappa;
s_dump = s; // this is the tether location before translation, note s = [s(0), s(1), s(2)).
s_dump(0) = s(0) - 7; // now the desired location is translated.
// apply tether force only if z-coordinate of original position is within 0.1 of center.
if (abs(s(2)) < .1)
{
kappa = kappa_s;
}
else
{ // no tether force, set tether stiffness to zero.
kappa = 0;
}
F = kappa * (s_dump - X); // Note x is actual position, s_dump is desired position
return;
}
Apply target force at the midline of plate using target_force_function. Applied in band running from -.1 to .1 in z-direction.

## Slide 15: main.C - stress tensor functions
We want the middle of the plate to have a different stiffness than the ends.
void PK1_dev_stress_function(TensorValue<double>& PP, const TensorValue<double>& FF,
const libMesh::Point& /*X*/, const libMesh::Point& s, Elem* const /*elem*/,
const vector<NumericVector<double>*>& /*system_data*/, double time, void* /*ctx*/)
{
double mu;
// lines below apply one stiffness value to middle, and the rest gets another stiffness
if (abs(s(2)) < .25)
{
mu = mu_stem;
}
else
{
mu = mu_leaf;
}

## Slide 16: main.C - stress tensor functions
Repeat for dilation stress function.
void PK1_dil_stress_function(TensorValue<double>& PP, const TensorValue<double>& FF,
const libMesh::Point& /*X*/, const libMesh::Point& s, Elem* const /*elem*/,
const vector<NumericVector<double>*>& /*system_data*/, double /*time*/, void* /*ctx*/)
{
double mu;
double beta;
// lines below apply one stiffness value to middle, and the rest gets another stiffness
if (abs(s(2)) < .25)
{
mu = mu_stem;
beta = beta_stem;
}
else
{
mu = mu_leaf;
beta = beta_leaf;
}