## Slide 1: 5-IBFE Lecture – Plans for June

## Slide 2: Updates
The 3D flow past a plate code from lecture 3 is now working. The example is available on github, along with the flow past the horseshoe crab.
There is now a new ibamr install on dogwood (as of this morning). I will update all of the examples for that install over the next month.
  WARNING: I have not tested this yet!

## Slide 3: Loading modules
To load the old module:
  module add ibamr
  module list
    Currently Loaded Modules:
    1) openmpi_2.0.3/gcc_4.8.5 2) ibamr/2018-03
To load the new module
  module add ibamr/0.6.0
  module list
    Currently Loaded Modules:
    1) openmpi_2.0.3/gcc_4.8.5 2) ibamr/0.6.0
To remove a module
  module rm ibamr

## Slide 4: Updating to the new ibamr install
I recommend installing your own updated version of ibamr as well.
I will work on updating the examples, and leave the old versions in a folder called ibamr-examples-2018-03.
Why move to the new install?
  There are some issues with two boundaries in the older IBAMR. How they are handled has changed since my last examples (ca. 2016), but 2018 is also different from 2020.
  There are numerous updates such as constraint-IB, sharp interface (e.g. immersed interface), that are not on this old install.

## Slide 5: Two boundaries – work in progress
Basic idea:
  Supplying an array of meshes.
  Specify parts to the registered functions.
There is an example from Boyce, but it only works on the newest install (I think).
  IBFE/examples/explicit/ex6
  https://github.com/IBAMR/IBAMR/tree/master/examples/IBFE/explicit/ex6
  This example has a sphere and a beam in 2D, but I have not run it yet.

## Slide 6: Things to change in main.C (under force declarations)
// Get various standard options set in the input file.
const string mesh1_exodus_filename = app_initializer->getExodusIIFilename("mesh1");
const string mesh2_exodus_filename = app_initializer->getExodusIIFilename("mesh2");
// Note that boundary condition data must be registered with each FE
// system before calling IBFEMethod::initializeFEData().
Mesh mesh1(NDIM);
Mesh mesh2(NDIM);
mesh1.read("IBFE_Mesh2D_128.mat");
mesh1.prepare_for_use();
mesh2.read("IBFE_Mesh2D_128.mat");
mesh2.prepare_for_use();
vector<Mesh*> meshes(2);
meshes[0] = &mesh1;
meshes[1] = &mesh2;
ca. 2016 approach for 2 boundaries

## Slide 7: Things to change in main.C (under force declarations) (continued…)
//Configure the IBFE Solver
IBFEMethod::LagBodyForceFcnData target1_force_data(target1_force_function);
IBFEMethod::LagBodyForceFcnData target2_force_data(target2_force_function);
ib_method_ops->registerInitialCoordinateMappingFunction(coordinate1_mapping_function, 0);
ib_method_ops->registerInitialCoordinateMappingFunction(coordinate2_mapping_function, 1);
ib_method_ops->registerLagBodyForceFunction(target1_force_data, 0);
ib_method_ops->registerLagBodyForceFunction(target2_force_data, 1);
ib_method_ops->registerPK1StressFunction(PK1_dev_stress_data, 0);
ib_method_ops->registerPK1StressFunction(PK1_dev_stress_data, 1);
ib_method_ops->registerPK1StressFunction(PK1_dil_stress_data, 0);
ib_method_ops->registerPK1StressFunction(PK1_dil_stress_data, 1);
EquationSystems* mesh1_equation_systems = ib_method_ops->getFEDataManager(0)->getEquationSystems();
EquationSystems* mesh2_equation_systems = ib_method_ops->getFEDataManager(1)->getEquationSystems();
ca. 2016 approach for 2 boundaries

## Slide 8: Things to change in main.C (under force declarations) (continued…)
//Setup visualization plot file writers
AutoPtr<ExodusII_IO> mesh1_exodus_io(uses_exodus ? new ExodusII_IO(mesh1) : NULL);
AutoPtr<ExodusII_IO> mesh2_exodus_io(uses_exodus ? new ExodusII_IO(mesh2) : NULL);
//Write out initial visualization data
if (uses_exodus) {
mesh1_exodus_io->write_timestep(mesh1_exodus_filename, *mesh1_equation_systems, iteration_num/viz_dump_interval+1, loop_time);
mesh2_exodus_io->write_timestep(mesh2_exodus_filename, *mesh2_equation_systems, iteration_num/viz_dump_interval+1, loop_time);
}
//In main time-loop (write visualization data)
if (uses_exodus){
mesh1_exodus_io->write_timestep(mesh1_exodus_filename, *mesh1_equation_systems, iteration_num/viz_dump_interval+1, loop_time);
mesh2_exodus_io->write_timestep(mesh2_exodus_filename, *mesh2_equation_systems, iteration_num/viz_dump_interval+1, loop_time);
}
ca. 2016 approach for 2 boundaries

## Slide 9: Other examples
Over the next month, I think it will be worth while for everyone to look at Boyce’s other examples:
  https://github.com/IBAMR/IBAMR/tree/master/examples/
As far as I know, there is no write up on what these examples are. So I would just try to run them and see what is available.

## Slide 10: Examples coming this month
Rotating and possibly flapping IBFE wing in 3D.
Pulsing coral in 3D (already given to coral team, let me know if you would like to see this).
Swimming sheet.

## Slide 11: Other things to do this month
Explore the various meshing programs.
Consider getting your own mesh software.
  Trellis: https://csimsoft.com/educational
  Bolt (better hex meshing): https://csimsoft.com/boltoverview
Cubit from Sandia National Labs (I haven’t used this)
  https://cubit.sandia.gov/

## Slide 12: Also, learn 3D CAD
You can mesh stl files (as well as others).
There are many stl files available online.
  You may need to smooth them to mesh them though.
  I recommend meshmixer (free for academics): http://www.meshmixer.com/
You can make your own stl files as well.
  I recommend to start using Tinkercad: https://www.tinkercad.com/
  And then move to Autodesk (free for academics): https://knowledge.autodesk.com/customer-service/account-management/education-program/free-education-access/licenses-for-educational-institutions