## Slide 1: 3-IBFE 3D Flow Past Objects

## Slide 2: Goal
Create a plate in a 3D flow tank.
Let the plate be tethered along its centerline.
Move the flow from left to right along x-axis.
See example 3-IBFE-Example_FlowTank-MidPlate.

## Slide 3: Strategy for domain and plate dimensions
In this example, the domain is 32x16x16 units.
The domain goes from -16<x<16, -8<y<8, -8<z<8.
dx = 16/256 = 0.0625.
Make a plate that is 0.125 x 2 x 2 units.
Previously, we translated the plate to the left. That feature is not working as it used to in newer versions of IBAMR.

## Slide 4: Step 1: Make the mesh in gmsh
The resulting file should be similar to plate2.msh in the Example folder.
Remember that we want the element size to be about dx=0.0625.
We can make this by making a square and then extruding it into the third dimension.

## Slide 5: Open gmsh, then File-> new
Go to Geometry-> Elementary entities -> Add -> Point
Make points at (0,1,1), (0,-1,1), (0,-1,-1) and (0,1,-1) with Prescribed mesh element size set to 0.0625.
Click Add for each point.

## Slide 6: Connect the points with lines
Go to Geometry-> Elementary entities-> Add-> Straight Line
Left click one point and then the next to make a line.
Repeat for all 4 sides.
Left click and drag to rotate the image in 3D.

## Slide 7: Make a surface from the square
Geometry-> Elementary entities -> Add->Plane Surface
Left click a line to illuminate the hole square.
Press e to end selection.
A grid should appear over the plane.

## Slide 8: Extrude to 3D plate
Geometry-> Elementary entities -> Add -> Translate -> Extrude surface
Extrude 0.125 in x-direction.
Left click grid so it’s red.
Press e to end.
This will make plate 2 elements thick.

## Slide 9: Make a volume in the frame
Geometry-> Add -> Elementary entities -> Add -> Volume
Select dashed grid lines so the glow red, click e to end.

## Slide 10: Add a physical group that is the volume
Geometry->Physical Groups -> Add -> Volume
In the popup box, name your mesh and use automatic numbering.
Left click the yellow dot in the middle of box.
Press ‘e’ to end.

## Slide 11: Make the mesh
Mesh -> 3D
File -> save mesh
The above will save the mesh of the physical group as group_name.msh. This leaves only the 3D mesh and no 1D or 2D meshes that libmesh will reject.

## Slide 12: input3d
In this example, the mesh name is given in both the input3d file and the main.C file.
Re is modified by updating the viscosity accordingly.
Flow ramps up from 0 m/s at t = 0 and moves in the x-direction.

## Slide 13: main.C- Target forces
voidtarget_force_function(
VectorValue<double>& F,
const TensorValue<double>& /*FF*/,
const libMesh::Point& X,
const libMesh::Point& s,
Elem* const /*elem*/,
const std::vector<const std::vector<double>*>& /*var_data*/,
const std::vector<const std::vector<VectorValue<double> >*>& /*grad_var_data*/, double time,
void* /*ctx*/)
{
Apply target force at the midline of plate using target_force_function. Applied in band running from -.1 to .1 in z-direction.

## Slide 14: main.C- Target forces
libMesh::Point s_dump;
double kappa;
s_dump = s;
// apply tether force only if z-coordinate of original position is within 0.1 of center.
if (abs(s(2)) < .1)
{
kappa = kappa_s;
}
else
{ // no tether force, set tether stiffness to zero.
kappa = 0;
}
F = kappa * (s - X); // Note x is actual position, s is desired position
return;
}

## Slide 15: main.C - stress tensor functions
void PK1_dev_stress_function(
TensorValue<double>& PP,
const TensorValue<double>& FF,
const libMesh::Point& X,
const libMesh::Point& s,
Elem* const /*elem*/,
const std::vector<const std::vector<double>*>& /*var_data*/,
const std::vector<const std::vector<VectorValue<double> >*>& /*grad_var_data*/,
double time,
void* /*ctx*/)
{
double mu;
mu = mu_stem;
PP = (mu)*FF;
return;
} // PK1_dev_stress_function

## Slide 16: main.C - stress tensor functions
Void PK1_dil_stress_function(
TensorValue<double>& PP,
const TensorValue<double>& FF,
const libMesh::Point& X,
const libMesh::Point& s,
Elem* const /*elem*/,
const std::vector<const std::vector<double>*>& /*var_data*/,
const std::vector<const std::vector<VectorValue<double> >*>& /*grad_var_data*/,
double time,
void* /*ctx*/)
{
double mu;
double beta;
mu = mu_stem;
beta = beta_stem;
PP = (-1.0*(mu)+beta*log(FF.det()))*tensor_inverse_transpose(FF,NDIM);
return;
} // PK1_dil_stress_function