## Slide 1: 2 – IB2d and IBAMR associated Files (.vertex, .spring, etc)

## Slide 2
What do the different input files do?
The input2d and input3d (IBAMR only) files include a lot of information on physical parameters (density, viscosity, boundary conditions, domain size) and numerical parameters (dt, dx, printing intervals, etc.)
In addition to the input2d/input3d files, there are a number of files that specify the initial conditions and material properties of the immersed elastic structures.
The only such file that is required is the ".vertex" file, which specifies the initial positions of the IB points.
There are several additional files that may be optionally specified:
    A ".spring" file can be used to specify an essentially arbitrary network of springs that connect the various IB points. Each "spring" connects precisely two IB points.
    A ".beam" file can be used to specify a collection of linear beams with a preferred curvature. Each "beam" connects precisely three IB points.
Input files
Notes: *

## Slide 3: Input files cont’d
A ".target" file is used to specify IB points that are, by default, "tethered" by stiff linear springs to their initial positions. Note that it is also possible to update the location to which each target point is tethered to within a simulation, so as to provide an approximately-prescribed motion for the target points.
A ".mass" file is used to specify any additional mass associated with the IB points. In IBAMR for such files to have any effect, it is necessary that the IB solver be run in "penalty-IB" mode.
A ".anchor" file (IBAMR only) is used to specify "anchor" points. In IBAMR, anchor points are IB points that neither apply force to the fluid nor interpolate velocity from the fluid. They are literally anchored in place. (Note: Anchor points are distinct from target points. Target points can be thought of as being tethered to anchor points.)

## Slide 4
Vertex file format
Vertex input files end with the extension ".vertex" and have the following format for two-dimensional models:
N # number of vertices in the file
x_0 y_0 # (x,y)-coordinates of vertex 0
x_1 y_1 # (x,y)-coordinates of vertex 1
...
x_{N-1} y_{N-1} # (x,y)-coordinates of vertex N-1
Vertex input files end with the extension ".vertex" and have the following format for three-dimensional models (IBAMR only):
N # number of vertices in the file
x_0 y_0 z_0 # (x,y,z)-coordinates of vertex 0
x_1 y_1 z_1 # (x,y,z)-coordinates of vertex 1
...
x_{N-1} y_{N-1} z_{N-1} # (x,y,z)-coordinates of vertex N-1

## Slide 5: IBAMR / ib2d differences
In IBAMR, you can have multiple .vertex, .beam, etc. files for different boundaries.
In ib2d, multiple boundaries are combined into one long list.
  This means that you have to keep track of where one boundary ends and the next starts.
  For example, assume you have two plates. Plate1 is defined by vertices 1-100 and Plate2 by vertices 101-200.

## Slide 6
Target point file format – ib2d
Target point input files end with the extension ".target" and have the following format:
The user provides a list of all target point indices with their associated target point stiffness.

## Slide 7
Target point file format - IBAMR
Target point input files end with the extension ".target" and have the following format:
M # number of target points in the file
i_0 kappa_0 eta_0
# vertex index, penalty spring constant, penalty damping coefficient
i_1 kappa_1 eta_1
i_2 kappa_2 eta_2
...
Note:
  Target points are anchored to their initial positions by linear springs with the specified spring constants and with zero resting lengths. Consequently, target points approximately enforce internal Dirichlet boundary conditions. The penalty parameter provides control over the energetic penalty imposed when the position of the Lagrangian immersed boundary point deviates from that of its specified fixed location.
  Damping coefficients are optional and are set to 0.0 if not supplied. Target points are "anchored" in place using Kelvin-Voigt viscoelastic elements.

## Slide 8
Spring file format (ib2d)
Spring input files end with the extension ".spring" and have the following format:
Note:
  A list of the master and slave nodes for each linear spring along with their associated spring stiffness, resting-length, and degree of non-linearity. Note that if using only Hookean springs, the degree of non-linearity can be omitted and IB2d will automatically assume linear springs.
  There is no restriction on the number of springs that may be associated with any particular node of the Lagrangian mesh.

## Slide 9
M # number of links in the file
i_0 j_0 kappa_0 length_0 fcn_idx_0
# first vertex index, second vertex index, spring constant,
# rest length, spring function index
i_1 j_1 kappa_1 length_1 fcn_idx_1
i_2 j_2 kappa_2 length_2 fcn_idx_2
...
Note:
  There is no restriction on the number of springs that may be associated with any particular node of the Lagrangian mesh.
  The rest length and force function index are optional values. If they are not provided, by default the rest length will be set to the value 0.0 and the force function index will be set to 0. This corresponds to a linear spring with zero rest length.
Spring file format (IBAMR)
Spring input files end with the extension ".spring" and have the following format:

## Slide 10: .beam file (torsional spring) – ib2d
Beam input files end with the extension ".beam" and have the following format:
This gives a list of the left, middle, and right Lagrangian indices associated with each torsional spring (beam) and their associated beam stiffness and curvature.

## Slide 11: .beam file (torsional spring) – ib2d

## Slide 12: .nonInv_beam file (beam equation) – ib2d
Another way to model the resistance bending between three successive Lagrangian points (rather than using torsional springs) is by using a non-invariant beam connecting the three successive nodes. The model assumes a prescribed ‘curvature’ in both x and y components between the three Lagrangian points with corresponding bending stiffness kNIB. The corresponding bending deformation forces are modeled as
Fbeam = kNIB ∂4/∂s4 (X(s, t) − Xb(s))
where X(s, t) is the current Lagrangian configuration at time t, e.g. the mapping of the Lagrangian points s to the underlying Cartesian grid, and Xb(s) is the preferred configuration of the fiber model.
This model is denoted as non-invariant beams since these beams are non-invariant under rotations, as opposed to the torsional spring fiber model. Similarly to the torsional spring model, non-invariant beam deformation forces can only occur on immersed boundary points on the interior or the fiber structure, not the endpoints.

## Slide 13
Beam file format (IBAMR)
Beam input files end with the extension ".beam" and have the following format:
M # number of beams in the file
i_0 j_0 k_0 kappa_0
# first vertex index, second vertex index, third vertex index,
# bending rigidity
i_1 j_1 k_1 kappa_1
# first vertex index, second vertex index, third vertex index,
# bending rigidity
i_2 j_2 k_2 kappa_2
# first vertex index, second vertex index, third vertex index,
#bending rigidity ...
Note that IBAMR beams are noninvariant beams.

## Slide 14
.mass: A list of all Lagrangian mass point indices along with their associated mass-spring stiffness and mass.
Mass point file format (ib2d)

## Slide 15
Mass point file format (IBAMR)
Mass point input files end with the extension ".mass" and have the following format:
M # number of mass points in the file
i_0 mass_0 kappa_0 # vertex index, point mass, penalty spring constant
i_1 mass_1 kappa_1
i_2 mass_2 kappa_2
...
Note:
  Mass points are anchored to "ghost" massive particles by linear springs with the specified spring constants and with zero resting lengths. The massive particles are "isolated" and simply move according to Newton's laws. The penalty parameter provides control over the energetic penalty imposed when the position of the Lagrangian immersed boundary point deviates from that of its massive copy.

## Slide 16: Input2d – ib2d

## Slide 17: Input2d IBAMR
There are more options in the IBAMR input2d/input3d files, and we will discuss these more in the future.
The main features that are relevant to our initial examples will be outlined here.

## Slide 18: Rubber band example
Analogous examples for ib2d and IBAMR are available on github:
  2-IBAMR-Example_2Drubber_band
  2-IB2d-Example_2Drubber_band
The MATLAB code creates the .vertex and .spring files for a rubber band that resists stretching. This can be used to create .vertex and .spring files for both ib2d and IBAMR.

## Slide 19
The rubber band is slightly deformed and will wobble as it returns to the shape of a perfect circle.

## Slide 21: generate_mesh2d.m
L = 1; % length of computational domain (m)
N = 512; % number of Cartesian grid meshwidths at the finest level of the AMR grid
dx = L/N; % Cartesian mesh width (m)
radius = 0.1; % radius of band (m)
epsilon = 0.005; % deformation in the x-direction
band_length = 2*pi*radius; % rubber band length (m)
npts = ceil(2*(band_length/L)*N); % number of points along the rubber band
ds = band_length/(npts); % physical distance between neighboring Lagrangian mesh points (m)
dtheta = 2*pi/npts;
mesh_name = 'rubber_band_'; % structure name
kappa_spring = 2.0e3; % spring constant (Newton)
kappa_beam = 5.0e-3; % beam stiffness constant (Newton m^2)

## Slide 22: Generate_mesh2d.m .vertex
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% Write out the vertex information
vertex_fid = fopen([mesh_name num2str(N) '.vertex'], 'w');
fprintf(vertex_fid, '%d\n', npts);
for s = 0:npts-1
X(1) = (radius+epsilon)*sin(s*dtheta);
X(2) = radius*cos(s*dtheta);
fprintf(vertex_fid, '%1.16e %1.16e\n', X(1), X(2));
end
fclose(vertex_fid);
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%

## Slide 23: rubber_band_512.vertex
644
0.0000000000000000e+00 1.0000000000000001e-01
1.0244161346221071e-03 9.9995240574191152e-02
2.0487347565924115e-03 9.9980962749807278e-02
3.0728583625411962e-03 9.9957167885933298e-02
4.0966894676620277e-03 9.9923858247566999e-02
5.1201306149911948e-03 9.9881037005403420e-02
6.1430843846844874e-03 9.9828708235533081e-02
7.1654534032904536e-03 9.9766876919053921e-02
8.1871403530192222e-03 9.9695548941597226e-02
9.2080479810060564e-03 9.9614731092767334e-02
1.0228079108568690e-02 9.9524431065495328e-02
1.1247136640457638e-02 9.9424657455306847e-02
1.2265123574098539e-02 9.9315419759503781e-02
1.3281943008825695e-02 9.9196728376260312e-02
1.4297498155105894e-02 9.9068594603633084e-02
1.5311692343751664e-02 9.8931030638485795e-02
1.6324429035123069e-02 9.8784049575328159e-02
1.7335611828317186e-02 9.8627665405069495e-02
1.8345144470344348e-02 9.8461893013686907e-02

## Slide 24: Generate_mesh2d.m .spring (ib2d)
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% Write out the spring information
spring_fid = fopen([mesh_name num2str(N) '.spring'], 'w');
fprintf(spring_fid, '%d\n', npts);
for s = 1:npts-1
fprintf(spring_fid, '%d %d %1.16e %1.16e\n', s, s+1, kappa_spring*ds/(ds^2), ds);
End
if s == npts
fprintf(spring_fid, '%d %d %1.16e %1.16e\n', npts, 1, kappa_spring*ds/(ds^2), ds);
end
fclose(spring_fid);
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%

## Slide 25: Generate_mesh2d.m .spring (IBAMR)
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% Write out the spring information
spring_fid = fopen([mesh_name num2str(N) '.spring'], 'w');
fprintf(spring_fid, '%d\n', npts);
for s = 0:npts-2
fprintf(spring_fid, '%d %d %1.16e %1.16e\n', s, s+1, kappa_spring*ds/(ds^2), ds);
End
if s == npts-1
fprintf(spring_fid, '%d %d %1.16e %1.16e\n', npts-1, 0, kappa_spring*ds/(ds^2), ds);
end
fclose(spring_fid);
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%

## Slide 26: rubber_band_512.spring –ib2d
644
1 2 2.0499156670236122e+06 9.7564989241919039e-04
2 3 2.0499156670236122e+06 9.7564989241919039e-04
3 4 2.0499156670236122e+06 9.7564989241919039e-04
4 5 2.0499156670236122e+06 9.7564989241919039e-04
5 6 2.0499156670236122e+06 9.7564989241919039e-04
6 7 2.0499156670236122e+06 9.7564989241919039e-04
7 8 2.0499156670236122e+06 9.7564989241919039e-04
8 9 2.0499156670236122e+06 9.7564989241919039e-04
9 10 2.0499156670236122e+06 9.7564989241919039e-04
10 11 2.0499156670236122e+06 9.7564989241919039e-04
11 12 2.0499156670236122e+06 9.7564989241919039e-04
12 13 2.0499156670236122e+06 9.7564989241919039e-04
13 14 2.0499156670236122e+06 9.7564989241919039e-04
14 15 2.0499156670236122e+06 9.7564989241919039e-04
15 16 2.0499156670236122e+06 9.7564989241919039e-04
16 17 2.0499156670236122e+06 9.7564989241919039e-04
17 18 2.0499156670236122e+06 9.7564989241919039e-04
18 19 2.0499156670236122e+06 9.7564989241919039e-04
19 20 2.0499156670236122e+06 9.7564989241919039e-04
20 21 2.0499156670236122e+06 9.7564989241919039e-04

## Slide 27: rubber_band_512.spring -IBAMR
644
0 1 2.0499156670236122e+06 9.7564989241919039e-04
1 2 2.0499156670236122e+06 9.7564989241919039e-04
2 3 2.0499156670236122e+06 9.7564989241919039e-04
3 4 2.0499156670236122e+06 9.7564989241919039e-04
4 5 2.0499156670236122e+06 9.7564989241919039e-04
5 6 2.0499156670236122e+06 9.7564989241919039e-04
6 7 2.0499156670236122e+06 9.7564989241919039e-04
7 8 2.0499156670236122e+06 9.7564989241919039e-04
8 9 2.0499156670236122e+06 9.7564989241919039e-04
9 10 2.0499156670236122e+06 9.7564989241919039e-04
10 11 2.0499156670236122e+06 9.7564989241919039e-04
11 12 2.0499156670236122e+06 9.7564989241919039e-04
12 13 2.0499156670236122e+06 9.7564989241919039e-04
13 14 2.0499156670236122e+06 9.7564989241919039e-04
14 15 2.0499156670236122e+06 9.7564989241919039e-04
15 16 2.0499156670236122e+06 9.7564989241919039e-04
16 17 2.0499156670236122e+06 9.7564989241919039e-04
17 18 2.0499156670236122e+06 9.7564989241919039e-04
18 19 2.0499156670236122e+06 9.7564989241919039e-04
19 20 2.0499156670236122e+06 9.7564989241919039e-04

## Slide 28: HW - Your own rubber band
Modify the rubber band example.
  Write your own generate_mesh.m file that puts down .vertex points and .springs.
  Make the rubber band 50% smaller and deform it initially in a different way.